リスト１：

Escape character is '^]'.

Kuroutoshikou KURO-BOX/HG (IESHIGE)

Linux/ppc 2.4.17_mvl21

KURO-BOX login: root

Password:

Linux (none) 2.4.17_mvl21 #24 2004年 10月 19日 金曜日 17:17:03 JST ppc unknown

root@KURO-BOX:~# ls /proc/bus	①

pci  usb

root@KURO-BOX:~# mount	②

/dev/hda1 on / type ext3 (rw,noatime,errors=remount-ro,errors=remount-ro)

proc on /proc type proc (rw)

devpts on /dev/pts type devpts (rw,gid=5,mode=620)

/dev/hda3 on /mnt type ext3 (rw,noatime)

/proc/bus/usb on /proc/bus/usb type usbdevfs (rw)

root@KURO-BOX:~# fdisk /dev/sda	③-1

The number of cylinders for this disk is set to 24792.

There is nothing wrong with that, but this is larger than 1024,

and could in certain setups cause problems with:

1) software that runs at boot time (e.g., old versions of LILO)

2) booting and partitioning software from other OSs

(e.g., DOS FDISK, OS/2 FDISK)

Command (m for help): p	③-2

Disk /dev/sda: 255 heads, 63 sectors, 24792 cylinders

Units = cylinders of 16065 * 512 bytes

Device Boot    Start       End    Blocks   Id  System

/dev/sda1             1     24792 199141708+   7  HPFS/NTFS

Command (m for help): d	③-3

Partition number (1-4): 1	③-4

Command (m for help): n	③-5

Command action

e   extended

p   primary partition (1-4)

Partition number (1-4): 1	③-6

First cylinder (1-24792, default 1): 	③-7

Using default value 1

Last cylinder or +size or +sizeM or +sizeK (1-24792, default 24792): 	③-8

Using default value 24792

Command (m for help): t	③-9

Partition number (1-4): 1	③-10

Hex code (type L to list codes): 83	③-11

Command (m for help): p	③-12

Disk /dev/sda: 255 heads, 63 sectors, 24792 cylinders

Units = cylinders of 16065 * 512 bytes

Device Boot    Start       End    Blocks   Id  System

/dev/sda1             1     24792 199141708+  83  Linux

Command (m for help): w	③-13

The partition table has been altered!

Calling ioctl() to re-read partition table.

WARNING: If you have created or modified any DOS 6.x

partitions, please see the fdisk manual page for additional

information.

Syncing disks.

root@KURO-BOX:~# mke2fs -j /dev/sda1	④

mke2fs 1.22, 22-Jun-2001 for EXT2 FS 0.5b, 95/08/09

Filesystem label=

OS type: Linux

Block size=4096 (log=2)

Fragment size=4096 (log=2)

24903680 inodes, 49785427 blocks

2489271 blocks (5.00%) reserved for the super user

First data block=0

1520 block groups

32768 blocks per group, 32768 fragments per group

16384 inodes per group

Superblock backups stored on blocks: 32768, 98304, 163840, 229376, 294912,

819200, 884736, 1605632, 2654208, 4096000, 7962624, 11239424, 20480000,

23887872

Writing inode tables: done

Creating journal (8192 blocks): done

Writing superblocks and filesystem accounting information: done

This filesystem will be automatically checked every 39 mounts or

180 days, whichever comes first.  Use tune2fs -c or -i to override.

root@KURO-BOX:~# mkdir /mnt2	⑤

root@KURO-BOX:~# mount /dev/sda1 /mnt2	⑥

root@KURO-BOX:~# df	⑦

Filesystem           1k-blocks      Used Available Use% Mounted on

/dev/hda1              2063504    122320   1836364   7% /

/dev/hda3            238947484     32832 238914652   1% /mnt

/dev/sda1            196015808     32828 186025896   1% /mnt2

root@KURO-BOX:~#

リスト２：

Dec 25 06:27:52 KURO-BOX murasaki.usb[265]: beep is defined as "off"

Dec 25 06:27:52 KURO-BOX murasaki.usb[265]: usb device is added

Dec 25 06:27:52 KURO-BOX murasaki.usb[265]: vendor:0x7f7 product:0x109 Dclass:0x0 Dsubclass:0x0 Dprotocol:0x0 Iclass:0x8 Isubclass:0x6 Iprotocol:0x50

Dec 25 06:27:52 KURO-BOX murasaki.usb[265]: The device match nothing in mapfile

Dec 25 06:27:52 KURO-BOX murasaki.usb[265]: Please change MODULE in following line to the appropriate module name, add it to /etc/murasaki/murasaki.usbmap

Dec 25 06:27:52 KURO-BOX murasaki.usb[265]: MODULE 0x0383 0x7f7 0x109 0 0 0x0 0x0 0x0 0x8 0x6 0x50 0x00000000

リスト３(変更前)：

# Sun Mar  9 00:32:31 PST 2003

# usb module  match_flags idVendor idProduct bcdDevice_lo bcdDevice_hi bDeviceClass bDeviceSubClass bDeviceProtocol bInterfaceClass bInterfaceSubClass bInterfaceProtocol driver_info

#

# HUB

none           0x0010     0x0000   0x0000    0x0          0x0          0x09         0x0             0x0             0x0             0x0

0x0                0x00000000

# Joystick

joydev         0x0070     0x0000   0x0000    0x0          0x0          0x03         0x0             0x0             0x0             0x0

0x0                0x00000000

# Philips PCVC740K

alias-740K     0x0003     0x0471   0x0311    0x0          0x0          0x00         0x00            0x00            0x00            0x00

0x00               0x00000000

：

：

：

(以下略)

リスト３(変更後)：

# Sun Mar  9 00:32:31 PST 2003

# usb module  match_flags idVendor idProduct bcdDevice_lo bcdDevice_hi bDeviceClass bDeviceSubClass bDeviceProtocol bInterfaceClass bInterfaceSubClass bInterfaceProtocol driver_info

#

# USBHDD

alias-usbhdd   0x0383     0x07f7   0x0109   0x0          0x0          0x00         0x0             0x0             0x8             0x6

0x50               0x00000000

# HUB

none           0x0010     0x0000   0x0000    0x0          0x0          0x09         0x0             0x0             0x0             0x0

0x0                0x00000000

# Joystick

joydev         0x0070     0x0000   0x0000    0x0          0x0          0x03         0x0             0x0             0x0             0x0

0x0                0x00000000

# Philips PCVC740K

alias-740K     0x0003     0x0471   0x0311    0x0          0x0          0x00         0x00            0x00            0x00            0x00

0x00               0x00000000

：

：

：

(以下略)

リスト４(変更不要)：

wacom: evdev

cpia_usb: cpia

audio: soundcore

iforce: hid

joydev: hid

alias-sr: usb-storage scsi_mod sr_mod

alias-UHA6400: usbserial vendor=0x04bf product=0x0117

alias-UPA9664: usbserial vendor=0x04bf product=0x0115

alias-740K: pwc size=qsif fps=30 fbufs=5 mbufs=4 compression=3

リスト５(変更前)：

[net]: net

リスト５(変更後)：

[net]: net

[usb]: murasaki_mount

リスト６：

root@KURO-BOX:~# cat /proc/scsi/scsi

Attached devices:

Host: scsi0 Channel: 00 Id: 00 Lun: 00

Vendor: Maxtor   Model: 6Y200P0          Rev: YAR4

Type:   Direct-Access                    RMB: HardDisk

ANSI SCSI revision: 02

root@KURO-BOX:~#

リスト７(変更前)：

# This file is mount table for "murasaki_mount"

# partition = 0 -> whole disk

# pattern partition mount fs

RATOC.*CompactFlash     0       /mnt/dos        vfat

Y-E.*FD                 0       /mnt/dos        vfat

リスト７(変更後)：

# This file is mount table for "murasaki_mount"

# partition = 0 -> whole disk

# pattern partition mount fs

RATOC.*CompactFlash     0       /mnt/dos        vfat

Y-E.*FD                 0       /mnt/dos        vfat

# Maxtor.*                1       /mnt2           ext3

リスト８：

case $1 in

start)

do_mount

;;

stop)

# You have to run 'umount' by hand.

;;

esac

リスト９：

stop)

sleep 10

umount /mnt2

;;

esac